Status LEDs

Name	Description	Number
PWR	Enabled at program startup, signals that the PI’s software is running.	0
HV	Displays the status of the high voltage boost converter. LED is on when the converter’s ENABLE is set.	1
HEARTBEAT	LED is toggled every second to indicate that the software is in working order. If something locks up or the software crashes, this will stop blinking.	2
RTC OK	Enabled if good data and checksums are received from the Real Time Clock on the auxiliary board.	3
NTP OK	Enabled if NTP (clock synchronization) server can be reached.	4
NET OK	Enabled if the internet can be reached (ping results?).	5
ALARM	Enabled if the ALARM mode is set.	6
AUDIO	Enabled if the Pi is currently playing audio.	7