Pin Mapping

Name	Description	Pin	BCM Port
STATUS_DAT	Status LEDs’ shift register data pin.	11	17
STATUS_CLK	Status LEDs’ shift register clock pin.	13	27
STATUS_LAT	Status LEDs’ shift register latch pin.	7	4
DISPLAY_DAT	Display board Nixie shift registers’ data pin.	16	23
DISPLAY_CLK	Display board Nixie shift registers’ clock pin.	18	24
DISPLAY_LAT	Display board Nixie shift registers’ latch pin.	10	15
DISPLAY_BLANK	PWM brightness control pin for the Nixie tube display.	12	18
BUTTON_LEFT	Status of the ‘<’ pushbutton, active low.	15	22
BUTTON_RIGHT	Status of the ‘>’ pushbutton, active low.	19	10
BUTTON_UP	Status of the ‘+’ pushbutton, active low.	21	9
BUTTON_DOWN	Status of the ‘-’ pushbutton, active low.	23	11
ENCODER_D1	Pin #1 for the encoded position of the main rotary switch.	22	25
ENCODER_D2	Pin #2 for the encoded position of the main rotary switch.	24	8
ENCODER_D3	Pin #3 for the encoded position of the main rotary switch.	26	7

Sources:

- https://pinout.xyz
- https://www.raspberrypi.org/documentation/hardware/raspberrypi/schematics/Raspberry-Pi-Rev-2.1-Model-AB-Schematics.pdf